## Slide 1: Micro-op Cache Presentation
Hawk Wang & Junshi Wang
2020.2.20

## Slide 2: Catalog
Trace Cache
Micro-op Cache
HW status
What we do

## Slide 3: Trace Cache – Background #1
Core producer/consumer model
IPC = Core instruction bandwidth = min(Front IPC, Back IPC)
Good design: balance frontipc and backipc
  Backipc : resource-centric(register file, execution unit, ROB/LSQ size)
  trend: enlarge resource, gain high performance
  frontipc :compatible Back IPC, low latency, high bandwidth

## Slide 4: Trace Cache – Background #2
Frontipc factors:
  Well studied, influence on latency, indirect on throughput
    Instruction cache hit ratio
    Branch prediction accuracy
  Not studied yet, trace cache focus
    Branch throughput: predict more branch(basic block) per cycle, currently only 1 basic block
    Non-contiguous instruction alignment: due to taken branch, program flow not same as contiguous layout in instruction cache
    Fetch unit latency: when fetch restarts(branch miss resolve), waste cycles that useful instructions to backend

## Slide 5: Trace Cache - motivation
Conventional Instruction Cache
  Predict only 1 basic block per cycle
  Fetch maximum 1 basic block’s instructions limited on fetch boundary
  according to [1], average basic block’s instruction number is 4-5 for integer benchmark ( SPEC92 & Instruction Benchmark Suite(IBS) ), float benchmark longer
Trace Cache
  A novel cache structure store dynamic program flow --- trace
  Trace means multiple “contiguous“ basic blocks. “contiguous” not means contiguous in memory layout, but contiguous on program flow

## Slide 6: Trace Cache – Initial Architecture #1
Store instruction not micro operation
Not in the critical path – not contribute to pipeline latency
Mainly on conditional branch, not for indirect branch, unconditional branch treated as specific condition branch (no predict result compare)
Big changes in conventional frontend architecture  IMPORTANT !!!

## Slide 7: Trace Cache – Initial Architecture #2
Big changes in conventional frontend architecture  IMPORTANT !!!
conventional architecture provide same fetch IPC as Trace cache
  Multiple branch predictor
    Direction predict Predict more condition direction per cycle, reduce accuracy
    BTB Provide more branch target address per cycle
  Interleave instruction cache organization provides parallel accesses on more instruction address

## Slide 8: Trace Cache – Initial Architecture #3
Trace Cache line structure
line store max(n insts, m branches)
  “Hit” means tag + bp_result match
  “branch flags” store trace bpu history result
  “branch mask” Number of branches in trace
    Last bit indicate trace whether end with branch

## Slide 9: Trace Cache – Initial Architecture #4
Micro-architecture

## Slide 10: Trace Cache – Design Issues #1
Trace Cache is HW cache component, many design issues related to cache issues
Cache related issues
  Size / Associativity Large is good, but more cost
  Indexing function Simple method only use fetch address; Path associativity: index = {fetch addr, predict result} or F(fetch addr, predict result). Ex, “ABC” and “ABD” will locate in different entry
  Fill mechanism Whether support outstanding misses. Simple method miss after miss will stall previous miss done Fill trace in speculative path or commit path
  Partial matches Hit partial predict result, whether provide trace prefix; more line bits, need store intermediate branch & fall-through target
  Replacement policy Good replacement will improve hit ratio, but from disclosed papers not focus on this issue

## Slide 11: Trace Cache – Design Issues #2
Trace specific issues
  Trace selection
    Trace structure instruct number and branch number, which hit will terminate current trace
    Trace end ret / indirect branch / exception will end current trace
  Structure improve trace cache hit rate
    Special structure store recent traces, exceed threshold update to trace cache
    Victim cache store useful but replacement traces

## Slide 12: Trace Cache – Aggressive architecture #1
Initial architecture work on instruction level, involve:
  Multiple branch predictor low accuracy than conventional branch predictor
Refine branch predictor on trace level, frontend work on trace-centric

## Slide 13: Trace Cache – Aggressive architecture #2
Trace identity
  Instead of fetch address
  trace identify = {fetch addr, branch outcome}
Trace predictor
  Return-History-Stack, correlated global predictor
  criteria
Trace Cache
  Index by trace identity, with folding
Trace buffers
  Treat as line fill buffer
Conventional instruction cache
  simple BPU(local branch)
More on correlated global predictor
Each entry = { trace identity, saturate counter}
only counter == 0, will update entry
hit counter + 1; miss counter - 2

## Slide 14: Trace Cache – real implement #1
Trace Cache involve in P4(NetBurst) microarchitecture [3][4]
Support for “SMC” issue, technology referred by micro-op cache
Replace L1 instruction cache totally, decode & fetch logic locate in L2 Cache
Store micro operations, not x86 instruction
VIVT(virtual index / virtual tag), need flush when task switch, no use “trace identity” technology
Provide Trace predictor (small) & conventional predictor (large)

## Slide 15: Trace Cache – real implement #2
Trace Cache involve in P4(NetBurst) microarchitecture [3][4]
Trace built in Trace cache with link-list by line data
  LA: only trace head has, used for tag a trace
  Next way / Prev way: indicate next link node position
  set (next (X+1)%S; prev X-1)%S )
  UIP/UIP_VALID: trigger MSROM address
  NLIP: next trace address

## Slide 16: Trace Cache – real implement #3
Trace Cache involve in P4(NetBurst) microarchitecture [3][4]
Line data termination condition
  Complex x86 instruction, trigger MSROM
  Line maximum contain up to 2 branch micro-op
  Can’t fit one x86 instruction
Trace termination condition
  Encounter indirect jmp, call, return
  Branch mis-prediction, exception / interrupt
  Exceed a trace capacity, maximum 64 sets

## Slide 17: Trace Cache – real implement #1
Performance: 12K micro-ops trace cache similar hit rate to 8KB to 16KB instruction cache
Pitfalls
  Low decode bandwidth, decode work on 64bit data, 1 x86 per cycle
  Trace cache has redundant trace pieces due to only trace head has location address
  More conflict on trace entries, especially for some trace will be broken by some body overwritten by another trace. Trace Cache used a replacement not same as conventional “LRU”

## Slide 18: Trace Cache – real implement #2
Intel some gens Core based on P4 [5]
 | Pentium 4 Northwood, SP Prestonia, DP Gallatin, MP | Pentium 5 Prescott, SP Nocona, DP | Pentium 6 “Yamhill”, SP Jayhawk, DP Potomac, MP
Trace Cache | 12k uOPs/ 80KB 256 sets / 8 ways 6 uOPs per trace-line 53bit per uOP | 16k uOPs / 128KB 512 sets / 8 ways 4 uOPs per trace-line 64bit per uOP | 16k uOPs / 128KB 512 sets / 8 ways 4 uOPs per trace-line 64bit per uOP
Trace Cache bandwidth | 3 uOPS / cycle | 4 uOPS / cycle | 4 uOPS / cycle
Trace Cache BP | 512 entires | 1024 entries | 1024 entries

## Slide 19: Micro-op Cache #1
Conclusion: Trace cache is replaced by micro-operation cache
Review trace cache design decision:
  Low decoder bandwidth, only decode 1 x86 / cycle, if trace miss, build latency high
  Inefficient storage usage, due to trace storage mechanism, many entries conflict, reduce trace hit ratio
  Small dedicated Trace predictor, maybe not very accuracy implement (not many disclosed document on this)
  Trace assumption, long trace assumption, but maybe in real application, long trace not always persistence
  Need a large state-machine sync trace cache stream / build mode, waste power

## Slide 20: Micro-op Cache #2
Micro-op Cache is implement improvement of Trace cache on x86 Core
How micro-op Cache improvement
  Reserved conventional frontend, micro-op Cache just a bypass path
  No trace predictor
  Trace assumption, trace only contain 1 basic block
Result:
  micro-op cache 1.5K uOPs similar hit ratio to 6KB instruction cache, while 12K uOPs trace cache similar hit ratio to 8KB-16KB instruction cache, improve storage efficiency about 4X or more. Intel claim micro-op cache hit ratio ~80%

## Slide 21: Micro-op Cache – Architecture [6] #1
As L0i cache, inclusion with L1i cache (“coherency”)
No big change in frontend design, just add bypass path
Power/clock-gating legacy decode path when micro-op cache hit consecutively
UC cache is serialization cache, reducing power

## Slide 22: Micro-op Cache – Architecture [6] #2
UC cache is serialization cache, reducing power
Work on “basic block”, not trace
  Predetermined instruction length (counted as line number, ex, 3 in Intel patent)
  Conditional / unconditional branch, call, return
  Complex instruction trigger MSROM
  Exception / interrupt
Next IP calculated by conventional BPU
Support SMC, same mechanism as Trace cache

## Slide 23: Micro-op Cache – Design Issues
Size / associativity
Fill Mechanism
  Speculative vs. commit fill
  Outstanding fill buffer
Replacement policy
Trace selection & organization
Trace line structure

## Slide 24: Micro-op Cache – real implementation #1
Introduced in Sandy-bridge microarchitecture [7][8]
Notes: Compare Trace Cache:
1 Improvement storage efficiency, how: line structure, simple assumption(on basic block, not trace)
2. Simple implementation, no trace predictor
3. Involve power-gating to reduce power due to bypass path

## Slide 25: Micro-op Cache – real implementation #2
Special features
  L1i evict, then micro-op cache related entries flushed
  Work on 32B instruction window, if partial match in 32B window, go to legacy decode path
  New line condition
    X86 not fit in one line capacity
    Branch misprediction, restart instruction fetch
    Block end indication condition
  Replacement: standard LRU policy
  Fill mechanism: outstanding, speculative
  VIVT, Line structure, store offset, support hit in “middle” of way
Notes: Compare Trace Cache:
1 Improvement storage efficiency, how: line structure, simple assumption(on basic block, not trace)
2. Simple implementation, no trace predictor
3. Involve power-gating to reduce power due to bypass path

## Slide 26: Micro-op Cache – real implementation #3
 | Sandybridge | Haswell | Skylake | Sunnycove
Micro-op cache | 1536 uOPs 8 ways, 32 sets 6 uOP per line Statically divide thread Inclusive with L1i $ 32B window | Same left | Same left Inclusive with L1i $ 64B window | 2304 uOPs 8ways, 48 sets 6 uOP per line Statically divide thread Inclusive with L1i $ 64B window
Micro-op cache bandwidth | 4 uOP per cycle | Same left | Same left | 5 uOP per cycle
Intel microarchitecture configuration

## Slide 27: Micro-op Cache – Conclude #1
Micro-op cache is implementation optimization on Trace cache
Many implementation issues need consideration
  SMC support (communication on iTLB & iCache), how to flush obsolete micro-ops [described in USA patent], belong to functionality, not performance
  Which power-gating policy used
    L1i $ lookup never power-gate, no penalty on frontend switch
    As current Intel does, incur 1-2T penalty
  Sync between MITE & Micro-op Cache (Intel current use a side-band synchronize signal along pipeline)
  Fill buffer design

## Slide 28: Micro-op Cache – Conclude #2
Micro-op cache is implementation optimization on Trace cache
Issues related to architecture (we can touch?)
  Size / associativity
  Trace selection vs. Instruction window
  Line structure
  Micro-op data array throughput design (how many r/w per cycle)

## Slide 29: HW status
Heard from HW guys discuss, not very sure
  Already explore size / associativity
  Already study line structure (how many uOPs stored), how about meta-info?
  Trace selection issue?
  More design specific issues should not start
How to explore
  Dump uOP sequences from RTL simulation environment, then use trace model to simulate

## Slide 30: What we do – Preparation
Preparation --- ready
  Not need an entire Core model, only a frontend model enough, based on Sniper
  Branch predictor --- ready
  X86 decoder --- ready, only need to know “number uOPs and whether trap instructions”

## Slide 31: What we do – Exploration Direction
Parameter Exploration
  Optimizing key parameters (design space).
  Trace-based simulation or profiling on workload.
  Example topics:
    Trace line VS. instruction window, line can contain more uOPs?
    Architecture parameters
  HW team may had finished these simulations.
Prototype Design
  Implementing and optimizing one micro-uop in detail simulator.
  Example topics:
    Switching between fetching pipeline, MSROM, micro-op cache.
    Coherence with L1 cache.
  HW team may lead us because they are more familiar with design. But they may not put a lot of effects.

## Slide 32: Reference
1. “Trace Cache: a Low Latency Approach to High Bandwidth Instruction Fetching”, Eric Rotenberg, 1996
2. “Trace Cache”, Leon Gu, Ppt Slides, 2003
3. “The microarchitecture of the Pentium 4 processors”, intel, 2001
4. USA patent, “TRACE BASED INSTRUCTION CACHE”, 1997
5. http://www.chip-architect.org/news/2003_04_20_Looking_at_Intels_Prescott_part2.html#48%20bit%20virtual%20addresses:%20The%20virtual%20Trace%20Cache%20tags
6. “Micro-operation Cache: a power aware frontend for variable instruction length ISA”, Baruch Solomen, Avi Mendelson, 2001
7. USA patent, “POWER REDUCTION FOR PROCESSOR FRONT-END BY CACHING DECODED INSTRUCTIONS”, 2005
8. USA patent, “METHOD AND APPARATUS FOR PIPELINE INCLUSION AND INSTRUCTION RESTARTS IN A MICRO-OP CACHE OF A PROCESSOR”, 2008